## Slide 1
01
FINAL YEAR PROJECT PROPOSAL DEFENSE
BuildScan 3D
Visual-Inertial 3D Gaussian Splatting for Construction Spatial Verification
ONE-LINE PROBLEM
Once construction work is concealed behind drywall or a pour, remote reviewers have no verifiable way to confirm built dimensions match the design.
TEAM
Muhammad Umair 23i-0662 Muhammad Tayyab 23i-0636 Zaid Fareed 23i-0829
Supervisor: Furqan Nasir Stream: A — Research-Derived
FAST School of Computing • National University of Computer and Emerging Sciences

## Slide 2
02
AGENDA
What We'll Cover
01
Problem & Motivation
The gap in current construction verification workflows
02
Existing Work & Research Gap
Prior systems, prior FYP, and the research basis
03
Technical Challenge
Why this is a Complex Computing Problem
04
Proposed Solution
Contribution, system architecture
05
Feasibility & Evaluation
POC evidence, evaluation plan, risks
06
Project Plan & Considerations
Team roles, timeline, ethics & legal

## Slide 3
03
SECTION 01 · PROBLEM & MOTIVATION
The Problem & Who It Affects
CAPTURE USERS (ON-SITE)
Construction site supervisors & QA inspectors
Record video documenting site conditions during routine, active-site work.
REVIEW USERS (REMOTE)
Project managers & civil engineers
Inspect 3D reconstructions remotely and extract dimensions to verify as-built progress.
CURRENT WORKFLOW
Manual 2D photography, walking active floors; a tape measure is held in-frame for scale, then collated into static reports for remote managers.
WHY IT FAILS
A 2D photo doesn't encode verifiable spatial coordinates. Once work is concealed behind drywall or a pour, dimensions can't be confirmed remotely.
$1.8T
Estimated annual global cost of “bad data” in construction — inaccurate, incomplete, or untimely information — directly driving 14% of avoidable rework ($88B). Autodesk & FMI Consulting (2021).

## Slide 4
04
SECTION 02 · EXISTING WORK & RESEARCH GAP
Existing Solutions & Prior FYP
Existing Approach | Provides | Limitation | Our Difference
Matterport (commercial reality capture) | Dedicated LiDAR hardware; accurate floor plans & 360° tours. | Costs several thousand $; scheduled sessions; fixed-viewpoint navigation only. | Standard smartphone video — no proprietary hardware dependency.
Consumer mobile AI scanners (Polycam, Luma AI) | On-device LiDAR + cloud NeRF/3DGS; captures in minutes. | Closed, black-box output; no measurable floor-plan extraction; geometrically inconsistent on low-texture walls. | Integrates 2D-to-3D semantic segmentation for automated dimension extraction.
Prior FAST FYP (F25-283-D-Roomora) | Mobile room scanning → standard 3D meshes + AI 2D-to-3D + local AR visualisation. | Meshes lack 3DGS photorealistic fidelity; no compression/delivery to a remote browser. | Cloud 3DGS pipeline with ARCore fusion + .ksplat compression for remote browser delivery.
Current manual workflow | Walking the site; disconnected 2D photos with a tape measure held in-frame. | No depth/spatial context; remote verification impossible; contributes to costly rework. | Automates spatial & dimensional extraction, replacing manual tape-measure estimation.

## Slide 5
05
SECTION 02 · EXISTING WORK & RESEARCH GAP
Research & Technical Basis
Source / Method | Main Finding | Decision Influenced
Kerbl et al., 2023 3D Gaussian Splatting (ACM TOG / SIGGRAPH) | Real-time photorealistic rendering from sparse point clouds; raw .ply output is typically hundreds of MB. | Adopt 3DGS as the core reconstruction method, requiring an automated .ksplat compression stage before web delivery.
VIGS-SLAM, 2025 Visual-Inertial Gaussian Splatting SLAM (ECCV) | Tightly coupling visual correspondences with IMU pre-integration reduces tracking loss in low-texture conditions. | Fuse ARCore inertial telemetry with visual tracking to stabilise pose estimation on featureless surfaces (bare drywall).
ContextGS / Compact 3DGS, 2024–25 (NeurIPS) | Heuristic pruning, opacity-gradient densification & context modelling reduce required 3DGS primitives. | Implement an adaptive Three.js viewer with level-of-detail & splat-budget management driven by client hardware.
GSemSplat, 2024 Semantic 3D Gaussian Splatting (arXiv) | Linking 2D semantic features to 3D Gaussians after training avoids the overhead of joint semantic/geometry training. | Run 2D semantic segmentation independently on keyframes; project bounding boxes onto geometry after training.

## Slide 6
06
SECTION 03 · TECHNICAL CHALLENGE
The Complex Computing Challenge
Extract navigable, dimensionally-usable 3D reconstructions from unconstrained, noisy smartphone video on active construction sites -maintaining tracking through featureless/reflective surfaces, balancing high-fidelity rendering against browser memory limits, and deriving structured measurements from unstructured point clouds where errors carry real engineering consequences.
SEOUL ACCORD CHARACTERISTICS MAPPING
1
Conflicting Requirements
CHALLENGE
High-fidelity 3DGS rendering vs. strict mobile-browser memory limits.
RESOLUTION
Automated .ksplat compression + adaptive Three.js splat budget.
3
Depth of Knowledge
CHALLENGE
3D coordinate transforms & non-Euclidean point-cloud geometry.
RESOLUTION
Multi-sensor data fusion + custom 2D-to-3D back-projection.
5
Beyond Standard Practice
CHALLENGE
Routine web/CRUD architecture cannot handle async, heavy-compute reconstruction.
RESOLUTION
GPU task scheduling via message queue + Dockerised cloud GPU workers.
8
Interdependence
CHALLENGE
Failure in one pipeline stage cascades through the rest.
RESOLUTION
End-to-end error tracking & validation checks across pipeline stages.

## Slide 7
07
SECTION 04 · PROPOSED SOLUTION
Proposed Solution & Contribution
IN ONE SENTENCE
An engineered capture-to-delivery pipeline that fuses inertial and visual tracking, compresses reconstructions for browser delivery, and projects semantic labels onto geometry to support dimensional measurement — evaluated against existing systems and physical tape-measurement baselines.
PROBLEM → APPROACH → CONTRIBUTION
a
Stabilise tracking
Fuses ARCore inertial telemetry with COLMAP structure-from-motion to stabilise camera tracking on featureless construction surfaces.
b
Enable browser delivery
Automated point-pruning and .ksplat compression keep reconstructions renderable in a standard web browser.
c
Support measurement
2D-to-3D semantic projection supports dimensional measurement directly from the reconstructed geometry.
The individual components — 3DGS, COLMAP, ARCore, Three.js — are established research and tooling. The pipeline that fuses them reliably under construction-site constraints and delivers within browser memory limits is the team's own engineering contribution.

## Slide 8
08
SECTION 04 · PROPOSED SOLUTION
System Architecture
STAGE 1 · ON-SITE CAPTURE
STAGE 2 · CLOUD RECONSTRUCTION
STAGE 3 · REMOTE DELIVERY
Capture User
(Site Supervisor / QA Inspector)
Android App — ARCore telemetry + edge image-quality validation (FR1–FR3)
Object Storage — raw video + telemetry (JSON)
Backend API (Node.js / Express)
Redis Job Queue (FR4)
COLMAP SfM + ARCore fusion (FR5)
3D Gaussian Splatting training (FR6)
2D semantic segmentation on keyframes (FR7)
Heuristic pruning + .ksplat compression (FR8)
Compressed Scene Storage (.ksplat) + Metadata DB
Web Backend (Next.js)
Browser Dashboard — Three.js / WebGL viewer (FR9–FR11)
Review User
(Project Manager / Civil Engineer)
Four cooperating layers: mobile capture (Android/ARCore) → backend orchestration (Redis-backed queue) → Dockerised GPU reconstruction worker (COLMAP, 3DGS, segmentation) → web review layer (Next.js + Three.js/WebGL).

## Slide 9
09
SECTION 05 · FEASIBILITY & EVALUATION
Feasibility Evidence (Proposal Stage)
HIGHEST-RISK ASSUMPTION
Whether a 3DGS reconstruction, once pruned and compressed into .ksplat format, can render smoothly inside a standard web browser rather than causing a memory failure.
PLANNED FEASIBILITY TEST
1
Record a short video of a low-texture indoor space
2
Process into a raw 3D Gaussian point cloud (local GPU / cloud notebook)
3
Compress the output into a .ksplat file
4
Confirm rendering in a browser-based viewer; record file-size reduction as evidence
EVIDENCE STATUS
[ INSERT POC SCREENSHOT / BASELINE RESULT — file-size reduction (.ply → .ksplat) and browser render confirmation to be added before defense ]

## Slide 10
10
SECTION 05 · FEASIBILITY & EVALUATION
Evaluation Plan
BASELINE / COMPARATOR
Current manual tape-measure workflow, plus qualitative comparison against Matterport, Polycam, and Luma AI.
DATA & SCENARIOS
Representative site captures spanning varied lighting and surface types — including featureless drywall and reflective/cluttered surfaces.
METRICS
The NFR targets: capture rate, edge-processing latency, pipeline latency, compression ratio, viewer frame rate, and dimensional accuracy (see below).
FAILURE CASES
Tracking loss on featureless/reflective surfaces; browser failure on an unpruned scene; incorrect material classification affecting dimension extraction.
NON-FUNCTIONAL TARGETS (USED AS EVALUATION METRICS)
≥ 30 FPS
Capture rate
< 16 ms / frame
Edge IQA latency
< 15 min (60s video, RTX 4090-class)
Pipeline latency
≥ 60% vs raw .ply
Compression ratio
≥ 30 FPS, mid-range browser
Viewer frame rate
within 5% of tape-measure baseline
Dimensional accuracy
User acceptance testing: a supervised task walkthrough in Semester 2 with the on-site construction stakeholder, documented per Section 13.1 of the FAST FYP guide.

## Slide 11
11
SECTION 05 · FEASIBILITY & EVALUATION
Risks & Mitigations
Type | Description | Mitigation
Risk | A user captures unusable, blurred, or dark video, wasting GPU cloud compute time. | Edge-based image-quality assessment (FR2) blocks poor uploads and prompts real-time capture correction.
Risk | ARCore hardware telemetry drifts over time, causing spatial warping in the reconstructed model. | Capture limited to short (~60s) segments to limit accumulated IMU drift and allow periodic spatial resets.
Assumption | The cloud GPU provider (RunPod) will remain highly available for processing. | Pipeline is containerised (Docker), allowing fallback to a local GPU environment if unavailable.
Issue | Standard 3DGS geometry can bleed across physical boundaries, complicating precise dimension extraction. | Semantic bounding boxes (FR7) enforce geometric separation between distinct materials before dimensions are calculated.
Dependency | Final-2 evaluation requires testing with a real construction stakeholder. | A local construction-site stakeholder has been engaged; formal confirmation & UAT scheduling to follow (Section 12).

## Slide 12
12
SECTION 06 · PROJECT PLAN & CONSIDERATIONS
Work Division & Team Responsibilities
Muhammad Umair
23i-0662
Mobile Edge Capture & Validation (Workflow A)
Native Android app with ARCore SDK for 6-DoF pose & IMU extraction
Real-time Image Quality Assessment (Laplacian variance + lux, <16ms)
Background async chunked video/telemetry upload to Cloudflare R2
Muhammad Tayyab
23i-0636
Cloud Orchestration & 3DGS Reconstruction Engine (Workflow B)
Distributed async task queue — Node.js/Express + Redis
Dockerised GPU worker containerisation on Ubuntu Linux
Sensor fusion (ARCore + COLMAP) and core 3DGS CUDA training
Zaid Fareed
23i-0829
Semantic AI, Compression & Web Delivery Portal (Workflows B & C)
2D CNN material segmentation + 2D-to-3D back-projection
Heuristic pruning + .ksplat compression engine (>60% reduction)
Next.js portal, Three.js viewer, dimension extraction, X-Ray overlay

## Slide 13
13
SECTION 06 · PROJECT PLAN & CONSIDERATIONS
Iteration Plan Across Two Semesters
SEMESTER 1 (FYP-1)
Core Build & Cloud Pipeline
Android app: ARCore telemetry + edge image-quality assessment (FR1–FR3)
Backend orchestration: Redis-backed async queue (FR4)
Dockerised cloud GPU infrastructure on Ubuntu Linux
Reconstruction engine: ARCore + COLMAP fusion, raw 3DGS point cloud (FR5–FR6)
Exit Gate (Final-1): a working core pipeline — mobile video → validated → spatially scaled 3D scene.
SEMESTER 2 (FYP-2)
Optimisation, Intelligence & Delivery
Compression engineering: heuristic pruning → .ksplat binaries (FR8)
Semantic AI integration: 2D-to-3D projection + planned X-Ray overlay (FR7, FR10, FR11)
Next.js + MongoDB web dashboard with adaptive Three.js viewer (FR9)
Formal user acceptance testing with named construction stakeholder
Exit Gate (Final-2): fully integrated, deployed platform with verifiable dimension extraction, having undergone UAT.
Optional Extension (not committed to core grade): Automated report generation comparing extracted 3D scan dimensions against uploaded 2D floor plans.

## Slide 14
14
SECTION 06 · PROJECT PLAN & CONSIDERATIONS
DEI, Ethics & Legal Considerations
DATA OWNERSHIP & CONSENT
On-site captures document active client construction sites. Formal confirmation of the on-site stakeholder's role and consent is required before Semester-2 UAT (Section 12).
SOFTWARE & MODEL LICENSING
Core-assist components — COLMAP, 3DGS CUDA kernels, pretrained YOLO/Mask2Former weights, Three.js — are used under their respective licenses; the team's own contribution is the fusion, compression, and semantic-projection pipeline.
RESPONSIBLE / RELIABLE AI
Semantic material misclassification can propagate into dimension extraction. Mitigated by enforcing semantic bounding-box separation (FR7) before measurement, as logged in the RAID register.
THIRD-PARTY DEPENDENCY RISK
Reliance on a cloud GPU provider (RunPod) is mitigated by a Dockerised pipeline that can fall back to a local GPU environment.
DIVERSITY, EQUITY & INCLUSION
[ADD DEI CONSIDERATION — not yet explicitly documented for this project]
DATA SECURITY
[ADD DATA SECURITY / ACCESS-CONTROL DETAIL — for cloud-stored site video & telemetry (Cloudflare R2 / object storage)]

## Slide 15
15
THANK YOU
Questions & Discussion
BuildScan 3D — Visual-Inertial 3D Gaussian Splatting for Construction Spatial Verification
Muhammad Umair (23i-0662) · Muhammad Tayyab (23i-0636) · Zaid Fareed (23i-0829)
Supervisor: Furqan Nasir · FAST School of Computing, NUCES